## Slide 1
최승식
Chap 2. Application Layer(3)

## Slide 2: Socket programming
Socket API
1981년 BSD4.1 UNIX에서 소개
응용에 의해 생성되고 사용후 해지
클라이언트/서버 패러다임
소켓API를 이용하여 2종류의 트랜스포트 서비스 이용:
  unreliable datagram(UDP)
  reliable, byte stream-oriented(TCP)
Goal: 소켓을 이용하여 클라이언트/서버응용 프로그램을 작성 함

## Slide 3: TCP를 이용한 소켓 프로그래밍
Socket: 응용 프로세스와 종단간 트랜스포트 프로토콜 사이의 도어 역할과 유사
TCP service: 프로세스간 신뢰성 있는 데이터 스트림 전달
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 4: UDP를 이용한 소켓 프로그래밍
UDP: 클라이언트와 서버사이에 연결 없슴(비연결형)
핸드세이크 과정이 없슴
송신호스트는 송신하는 각 바이트 묶음에 IP주소와 포트번호를 붙여서 패킷 생성
서버호스트는 수신된 패킷으로부터 IP어드레스와 포트 추출
UDP: 전송된 데이터가 손실될 수 있슴

## Slide 5: Client/server socket interaction: UDP
close
clientSocket
read datagram from
clientSocket
create socket:
clientSocket =
socket(AF_INET,SOCK_DGRAM)
Create datagram with server IP and
port=x; send datagram via clientSocket
create socket, port= x:
serverSocket =
socket(AF_INET,SOCK_DGRAM)
read datagram from
serverSocket
write reply to
serverSocket
specifying client address,
port number
server (running on serverIP)
client

## Slide 6
Example app: UDP client
from socket import *
serverName = ‘hostname’
serverPort = 12000
clientSocket = socket(AF_INET, SOCK_DGRAM)
message = raw_input(’Input lowercase sentence:’)
clientSocket.sendto(message.encode(),
(serverName, serverPort))
modifiedMessage, serverAddress =
clientSocket.recvfrom(2048)
print modifiedMessage.decode()
clientSocket.close()
Python UDPClient
include Python’s socket
library
create UDP socket for server
get user keyboard
input
Attach server name, port to message; send into socket
print out received string and close socket
read reply characters from
socket into string

## Slide 7
Example app: UDP server
from socket import *
serverPort = 12000
serverSocket = socket(AF_INET, SOCK_DGRAM)
serverSocket.bind(('', serverPort))
print (“The server is ready to receive”)
while True:
message, clientAddress = serverSocket.recvfrom(2048)
modifiedMessage = message.decode().upper()
serverSocket.sendto(modifiedMessage.encode(),
clientAddress)
Python UDPServer
create UDP socket
bind socket to local port number 12000
loop forever
Read from UDP socket into message, getting client’s address (client IP and port)
send upper case string back to this client

## Slide 8: TCP를 이용한 소켓 프로그래밍
서버 준비
서버 프로세스가 먼저 실행
서버는 클라이언트로 부터 초기접속을 처리하는 소켓을 가져야 함(서버소켓)
클라이언트 프로세스는 서버에게 TCP연결 시작
클라이언트는 소켓 객체를 생성
소켓객체를 생성시 서버의 IP주소와 프로세스의 포트번호를 명시
클라이언트가 소켓을 생성시 클라이언트 TCP는 서버 TCP와 3방향 핸드세이크로 연결을 설정함
서버는 클라이언트가 연결을 요청하면 서버는 클라이언트와의 통신을 위한 새로운 소켓을 생성함(연결소켓)

## Slide 9: Client/server socket interaction: TCP
wait for incoming
connection request
connectionSocket =
serverSocket.accept()
create socket,
port=x, for incoming request:
serverSocket = socket()
create socket,
connect to hostid, port=x
clientSocket = socket()
server (running on hostid)
client
send request using
clientSocket
read request from
connectionSocket
write reply to
connectionSocket
TCP
connection setup
close
connectionSocket
read reply from
clientSocket
close
clientSocket

## Slide 10
Example app: TCP client
from socket import *
serverName = ’servername’
serverPort = 12000
clientSocket = socket(AF_INET, SOCK_STREAM)
clientSocket.connect((serverName,serverPort))
sentence = raw_input(‘Input lowercase sentence:’)
clientSocket.send(sentence.encode())
modifiedSentence = clientSocket.recv(1024)
print (‘From Server:’, modifiedSentence.decode())
clientSocket.close()
Python TCPClient
create TCP socket for server, remote port 12000
No need to attach server name, port

## Slide 11
Example app: TCP server
from socket import *
serverPort = 12000
serverSocket = socket(AF_INET,SOCK_STREAM)
serverSocket.bind((‘’,serverPort))
serverSocket.listen(1)
print (‘The server is ready to receive’)
while True:
connectionSocket, addr = serverSocket.accept()
sentence = connectionSocket.recv(1024).decode()
capitalizedSentence = sentence.upper()
connectionSocket.send(capitalizedSentence.
encode())
connectionSocket.close()
Python TCPServer
create TCP welcoming
socket
server begins listening for incoming TCP requests
loop forever
server waits on accept()
for incoming requests, new socket created on return
read bytes from socket (but not address as in UDP)
close connection to this client (but not welcoming socket)

## Slide 12: Webserver Example
# Import socket module
from socket import *
import sys # In order to terminate the program
serverSocket = socket(AF_INET, SOCK_STREAM)
# Assign a port number
serverPort = 6789
# Bind the socket to server address and server port
serverSocket.bind(('', serverPort))
# Listen to at most 1 connection at a time
serverSocket.listen(1)
# Server should be up and running and listening to the incoming connections
while True:
print('The server is ready to receive')
# Set up a new connection from the client
connectionSocket, addr = serverSocket.accept()
try:
# Receives the request message from the client
message = connectionSocket.recv(2048).decode()
print(message)

## Slide 13: Webserver Example
try:
# Receives the request message from the client
message = connectionSocket.recv(2048).decode()
print(message)filename = message.split()[1]
print(filename)
myfile = open(filename[1:],'rb')
response = myfile.read()
myfile.close()
# Send the HTTP response header line to the connection socket
header = 'HTTP/1.1 200 OK\n'
if(filename.endswith(".jpg")):
filetype = 'image/jpg'
elif(filename.endswith(".mp4")):
filetype = 'video/mp4'
else:
filetype = 'text/html'
header += 'Content-Type: '+str(filetype)+'\n\n'
print(header)
connectionSocket.send(header.encode())
connectionSocket.send(response)
connectionSocket.close()

## Slide 14: Webserver Example
except IOError:
header = 'HTTP/1.1 404 Not Found\n\n'
response = '<html><body><center><h3>Error 404: File not found</h3>
<p>Python HTTP Server</p></center></body></html>'.encode()
print(header)
connectionSocket.send(header.encode())
connectionSocket.send(response)
connectionSocket.close()
serverSocket.close()
sys.exit()